## Slide 1: Antennas and Propagation
Lecture 2
G. Noubir
noubir@ccs.neu.edu
Textbook: Wireless Communications and Networks, William Stallings, Prentice Hall

## Slide 2: Outline
Antennas
Propagation Modes
Line of Sight Transmission
Fading in Mobile Environment and Compensation

## Slide 3: Decibels
The Decibel Unit:
  Standard unit describing transmission gain (loss) and relative power levels
  Gain: N(dB) = 10 log(P2/P1)
  Decibels above or below 1W: N (dBW) = 10 log(P2/1W)
  Decibels above or below 1Milliwatt: N(dBm) = 10log(P2/1mW)
Example:
  P = 1mW => P(dBm) = ? ; P(dBW) = ?
  P = 10mW => P(dBm) = ? ; P(dBW) = ?

## Slide 4: Introduction
An antenna is an electrical conductor or system of conductors
  Transmission - radiates electromagnetic energy into space
  Reception - collects electromagnetic energy from space
In two-way communication, the same antenna can be used for transmission and reception

## Slide 5: Basics of Radio-waves Propagation
Radiowave propagation:
  Radiowaves: electromagnetic waves
  Signal energy: electrical field (E) and magnetic field (H)
  E and H are sinusoidal functions of time
  The signal is attenuated and affected by the medium
Antennas
  Form the link between the guided part and the free space: couple energy
  Purpose:
    Transmission: efficiently transform the electrical signal into radiated electromagnetic wave (radio/microwave)
    Reception: efficiently accept the received radiated energy and convert it to an electrical signal
Notes: Disturbance that propagates without moving it’s medium
EM don’t need matter to propagate
Radiowaves: from 30KHz to 300 GHz
L = c/f => 10Km, 1mm.

## Slide 6: Radiation Patterns
Radiation pattern
  Graphical representation of radiation properties of an antenna
  Depicted as two-dimensional cross section
Beam width (or half-power beam width)
  Measure of directivity of antenna
Reception pattern
  Receiving antenna’s equivalent to radiation pattern
Notes: examples

## Slide 7: Types of Antennas
Theoretical reference antenna (isotropic radiator):
  A point in space radiating with equal power in all directions
  Points with equal power are located on a sphere with the antenna in the center
Real antennas exhibit directive effects:
  Types: omnidirectional (dipole) or directional (pencil beam)
  Simplest antenna:
    Dipole (or Hertzian dipole) of length /4 or /2
  Directional antennas may be more useful:
    To cover a highway, valley, satellite beam
  Parabolic antenna
Notes: Page 103
Parabolic definition
What it is it used for

## Slide 8: Antenna Gain
Antenna gain
  Power output, in a particular direction, compared to that produced in any direction by a perfect omnidirectional antenna (isotropic antenna)
  G = 4*PwrDirection/AllRadiatedPwr
Effective area
  Related to physical size and shape of antenna

## Slide 9: Antenna Gain
Relationship between antenna gain and effective area
    G = antenna gain
    Ae = effective area
    f = carrier frequency
    c = speed of light (» 3 ´ 108 m/s)
     = carrier wavelength
  Affective area:
    Isotropic: 2/4
    Half-wave dipole: 1.642/4 (power gain vs. istropic 1.64)
    Parabolic: 0.56 A (power gain vs. istropic 7A/2)
Notes: For a parabolic reflective antenna with a diameter of 2m operating at 12GHz. What is the effective area and antenna gain:
A = pi r^2 = 3.14
Ae = 0.56pi
Lambda = c/f = 0.025 m
G = 7A/l^2 => G = 35.186 = 45.46 dB

## Slide 10: Propagation Modes
Ground-wave propagation
Sky-wave propagation
Line-of-sight propagation

## Slide 11: Ground Wave Propagation
Notes: Current induced on earth surface

## Slide 12: Ground Wave Propagation
Follows contour of the earth
Can Propagate considerable distances
Frequencies up to 2 MHz
Example
  AM radio

## Slide 13: Sky Wave Propagation
Notes: Up to 30 MHz

## Slide 14: Sky Wave Propagation
Signal reflected from ionized layer of atmosphere back down to earth
Signal can travel a number of hops, back and forth between ionosphere and earth’s surface
Reflection effect caused by refraction
Examples
  Amateur radio
  CB radio

## Slide 15: Line-of-Sight Propagation

## Slide 16: Line-of-Sight Propagation
Transmitting and receiving antennas must be within line of sight
  Satellite communication – signal above 30 MHz not reflected by ionosphere
  Ground communication – antennas within effective line of site due to refraction
Refraction – bending of microwaves by the atmosphere
  Velocity of electromagnetic wave is a function of the density of the medium
  When wave changes medium, speed changes
  Wave bends at the boundary between mediums
Notes: Example with water and a running person

## Slide 17: Line-of-Sight Equations
Optical line of sight
Effective, or radio, line of sight
    d = distance between antenna and horizon (km)
    h = antenna height (m)
    K = adjustment factor to account for refraction, rule of thumb K = 4/3
Notes: R = 12.734/2

## Slide 18: Line-of-Sight Equations
Maximum distance between two antennas for LOS propagation:
    h1 = height of antenna one
    h2 = height of antenna two
Notes: Maximum distance between two antennas
H1 = 100m, h2 = 0 => 41km
If h2 = 10m => h1 = 46.2m

## Slide 19: LOS Wireless Transmission Impairments
Attenuation and attenuation distortion
Free space loss
Noise
Atmospheric absorption
Multipath
Refraction

## Slide 20: Attenuation (Pathloss)
Strength of signal falls off with distance over transmission medium
Attenuation factors for unguided media:
  Received signal must have sufficient strength so that circuitry in the receiver can interpret the signal
  Signal must maintain a level sufficiently higher than noise to be received without error
  Attenuation is greater at higher frequencies, causing distortion

## Slide 21: Free Space Loss
Free space loss, ideal isotropic antenna
    Pt = signal power at transmitting antenna
    Pr = signal power at receiving antenna
     = carrier wavelength
    d = propagation distance between antennas
    c = speed of light (» 3 ´ 10 8 m/s)
    where d and  are in the same units (e.g., meters)
Notes: 6dB loss every time the distance is doubled

## Slide 22: Free Space Loss
Free space loss equation can be recast:

## Slide 23: Free Space Loss
Free space loss accounting for gain of other antennas
    Gt = gain of transmitting antenna
    Gr = gain of receiving antenna
    At = effective area of transmitting antenna
    Ar = effective area of receiving antenna
Notes: Exercice: A transmitter produces 50W,
Pt in dBm: 47dBm, in dBW: 17dBW?
Pr at 100m: -24.5dBm, at 10km: -64.5dBm? (40dB difference)

## Slide 24: Free Space Loss
Free space loss accounting for gain of other antennas can be recast as

## Slide 25: Categories of Noise
Thermal Noise
Intermodulation noise
Crosstalk
Impulse Noise
Notes: Determining factors in communication:
  Absolute signal level, external noise, internal noise (tx/rx eq.)
Channel capacity depends on Signal Noise Ratio SNR
At HF (upto 30MHz):
  the noise in the propagation medium predominates
At VHF (from 30MHz - above):
  Tx and Rx noise (amplification at receiver) predominates
Sources of external noise: galactic, atmospheric, man
A passive load induces noise:
  N (W) = kT0B (k = 1.38 10-23, T0: temperature (290K), B: bandwidth)
Using an antenna:
  N (W) = Fa kT0B = (1+Te/T0)kT0B

## Slide 26: Thermal Noise
Thermal noise due to agitation of electrons
Present in all electronic devices and transmission media
Cannot be eliminated
Function of temperature
Particularly significant for satellite communication

## Slide 27: Thermal Noise
Amount of thermal noise to be found in a bandwidth of 1Hz in any device or conductor is:
    N0 = noise power density in watts per 1 Hz of bandwidth
    k = Boltzmann's constant = 1.3803 ´ 10-23 J/K
    T = temperature, in kelvins (absolute temperature)

## Slide 28: Thermal Noise
Noise is assumed to be independent of frequency
Thermal noise present in a bandwidth of B Hertz (in watts):
    or, in decibel-watts
Notes: Example: T = 290K => N0 = 4 10^-21W/H = -204dbW/H

## Slide 29: Noise Terminology
Intermodulation noise – occurs if signals with different frequencies share the same medium
  Interference caused by a signal produced at a frequency that is the sum or difference of original frequencies
Crosstalk – unwanted coupling between signal paths
Impulse noise – irregular pulses or noise spikes
  Short duration and of relatively high amplitude
  Caused by external electromagnetic disturbances, or faults and flaws in the communications system
Notes: Cos a + cos

## Slide 30: Expression Eb/N0
Ratio of signal energy per bit to noise power density per Hertz
The bit error rate for digital data is a function of Eb/N0
  Given a value for Eb/N0 to achieve a desired error rate, parameters of this formula can be selected
  As bit rate R increases, transmitted signal power must increase to maintain required Eb/N0

## Slide 31: Other Impairments
Atmospheric absorption – water vapor and oxygen contribute to attenuation
Multipath – obstacles reflect signals so that multiple copies with varying delays are received
Refraction – bending of radio waves as they propagate through the atmosphere

## Slide 32: Multipath Propagation

## Slide 33: Multipath Propagation
Reflection - occurs when signal encounters a surface that is large relative to the wavelength of the signal
Diffraction - occurs at the edge of an impenetrable body that is large compared to wavelength of radio wave
Scattering – occurs when incoming signal hits an object whose size in the order of the wavelength of the signal or less
Notes:   Reflection: Occurs when a radio wave propagating in one medium impinges upon another medium: partial reflection + partial transmission
    Second medium is a conductor: all incident energy is reflected
    Second medium is a dielectric: partial reflection and partial transmission in the second medium
  Diffraction: Occurs when the radio path is obstructed with a surface that has sharp irregularities (edges)
    Models: knife-edge and multiple knife-edge
  Scattering: Occurs when the medium consists of small objects (vs. )
    Reflected energy on rough surfaces is spread out (diffused) in all directions
    A surface is rough if: protuberance > hc = /(8 sin i)

## Slide 34: The Effects of Multipath Propagation
Multiple copies of a signal may arrive at different phases
  If phases add destructively, the signal level relative to noise declines, making detection more difficult
Intersymbol interference (ISI)
  One or more delayed copies of a pulse may arrive at the same time as the primary pulse for a subsequent bit

## Slide 35: Types of Fading
Fast fading
Slow fading
Flat fading
Selective fading
Rayleigh fading
Rician fading
Notes: Fast fading:
AWGN
Rayleigh: no distinct LOS
Rician: LOS + multipath
K = power in dominant path/power in the scattered path

## Slide 36: Radio Propagation
Large scale path loss + small-scale fading
Large scale path loss
  Outdoor propagation
    Long distance
    Takes into account terrain profile (e.g., mountains, hills, large buildings, etc.)
  Indoor propagation (inside buildings)
    Distances covered are much smaller and the environment is more variable
    Increasing interest due to PCS and WLAN
    Classified as line-of-sight (LOS) or obstructed (OBS)
Small-scale fading: multi-path

## Slide 37: Path Loss Models
Log-distance path loss model: average path loss
Log-normal shadowing (signal level at a specific distance have Gaussian distribution)
Environment
Path Loss Exponent n
Free space
2
Urban area PCS
2.7 to 3.5
Shadowed urban PCS
3 to 5
In building LOS
1.6 to 1.8
Obstructed in building
4 to 6
Obstructed in factories
2 to 3
Notes: In practice values of n and s are computed from measured data

## Slide 38: Path Loss Models of Outdoor
Okumura-Hata empirical model:
  Valid for f from 150MHz to 1500 MHz. For urban area:
  f: freq, hb: BS height, hm: mobile height, d: BS-MS distance
  For a small to medium sized city:
  For a large city:
  For suburban area:
  For rural area:
Notes: Measurement in Tokyo area by Okumura

## Slide 39: Other Path Loss Models
Euro-COST Extension of Okumura-Hata to PCS (f>1500MHz):
  CM = 0dB (medium and suburban), 3dB (metropolitan)
Walfish and Bertoni Model
  Integrates effect of diffraction on rooftops

## Slide 40: Path Loss Models for Indoor
Partition losses (same floor with soft or hard partitions)
  Uses estimation of path loss for each material at working frequency
Partition losses between floors
  Uses estimates of path loss
Ericsson Multiple breakpoint model:
  4 breakpoints, range of path-loss: [PLmin, PLmax]
Log-distance path loss:
  PL(dB) = PL(d0) + 10 n log(d/d0) + X
  n depend on surrounding environment, X is a normal random variable with standard deviation 
Attenuation factor model (average path loss)
  PL(dB) = PL(d0) + 10 nSF log(d/d0) + FAF (dB) = PL(d0) + 10 nMF log(d/d0)
Buildings penetration: depends on building height, number of windows, etc.
Ray tracing using Geographical Information System (GIS) databases
Notes: All these models use tables
Depends on building height, number of windows
SF single floor, MF: multiple floor

## Slide 41: Small Scale Fading Models
Multi-path fading:
  Multiple reflections from various objects: multiple path => multiple phase shifts
  Signal strength may vary by as much as 30-40dB in hostile environments when the receiver moves by only a fraction of 
  Main effects:
    Rapid change in signal strength over a small travel distance
    Random frequency modulation due to varying Doppler shifts on different multi-path signals
    Time dispersion (echoes) caused by multipath propagation

## Slide 42: Small Scale Fading (Cont’d)
Factors:
  Multipath propagation: multiple version of the signal with different shifts that may add or subtract
  Speed of the mobile: the relative speed between the mobile and BS results in random frequency modulation due to different incidence angles of paths
  Speed of surrounding objects
  Transmission bandwidth of the signal versus channel bandwidth (coherence bandwidth)
Characteristics:
  Long-term fading x short-term fading: s(t) = m(t)r(t)

## Slide 43: Fading Statistics
Doppler shift: fd = (v/) cos 
   is the angle between the radio wave propagation axis and the mobile trajectory
Level crossing rate (LCR):
  Average number of times per second that the signal envelope crosses the level in a positive direction
LCR and level crossing duration are important for estimating fading rate and duration => designing error control codes:
   = R(Specified level)/Rrms ; fm: max Doppler shift
  =>
  Average fade duration:

## Slide 44: Bit Error Rate
Bit Error Rate (BER): rate of bit errors
Estimating the BER is very important: it determines the packet loss (Frame Error Rate: FER)
Bit Error Rate is a function of the received energy per bit
Estimating path loss statistics allows to estimate the BER
Shannon’s Theorem (AWGN):
  A channel with a given SNR has maximum capacity: C = W log (1 + SNR)
  There exist a coding scheme that allows to achieve the channel capacity
Notes: What is the Eb/N0 required to achieve 6bps/H => (1/6)(2^6-1) = 10.5 = 10.21 dB

## Slide 45: Error Compensation Mechanisms
Forward error correction
Adaptive equalization
Diversity techniques

## Slide 46: Forward Error Correction
Transmitter adds error-correcting code to data block
  Code is a function of the data bits
Receiver calculates error-correcting code from incoming data bits
  If calculated code matches incoming code, no error occurred
  If error-correcting codes don’t match, receiver attempts to determine bits in error and correct

## Slide 47: Adaptive Equalization
Can be applied to transmissions that carry analog or digital information
  Analog voice or video
  Digital data, digitized voice or video
Used to combat intersymbol interference
Involves gathering dispersed symbol energy back into its original time interval
Techniques
  Lumped analog circuits
  Sophisticated digital signal processing algorithms

## Slide 48: Diversity Techniques
Diversity is based on the fact that individual channels experience independent fading events
Space diversity – techniques involving physical transmission path
Frequency diversity – techniques where the signal is spread out over a larger frequency bandwidth or carried on multiple frequency carriers
Time diversity – techniques aimed at spreading the data out over time`