## Slide 1: Bluetooth Techniques
Lecture 6

## Slide 2: Bluetooth
Consortium: Ericsson, Intel, IBM, Nokia, Toshiba - many other members
Scenarios:
  connection of peripheral devices
    loudspeaker, joystick, headset
  support of ad-hoc networking
    small devices, low-cost
  bridging of networks
    e.g., GSM via mobile phone - Bluetooth - laptop
Simple, cheap, replacement of IrDA, low range, lower data rates, low-power
  Worldwide operation: 2.4 GHz,
  Resistance to jamming and selective frequency fading:
    FHSS over 79 channels (of 1MHz each), 1600hops/s
  Coexistence of multiple piconets: CDMA
  Links: synchronous connections SCO (e.g., voice) and asynchronous connectionless ACL
  Interoperability: protocol stack supporting TCP/IP, OBEX, SDP
  Range: 10 meters, can be extended to 100 meters
Documentation: over 1000 pages specification: www.bluetooth.com

## Slide 3: Bluetooth Application Areas
Data and voice access points
  Real-time voice and data transmissions
Cable replacement
  Eliminates need for numerous cable attachments for connection
Low cost < $5
Ad hoc networking
  Device with Bluetooth radio can establish connection with another when in range

## Slide 4: Bluetooth Standards Documents
Core specifications
  Details of various layers of Bluetooth protocol architecture
Profile specifications
  Use of Bluetooth technology to support various applications

## Slide 5: Protocol Architecture
Bluetooth is a layered protocol architecture
  Core protocols
  Cable replacement and telephony control protocols
  Adopted protocols
Core protocols
  Radio
  Baseband
  Link manager protocol (LMP)
  Logical link control and adaptation protocol (L2CAP)
  Service discovery protocol (SDP)

## Slide 6: Protocol Architecture
Cable replacement protocol
  RFCOMM
Telephony control protocol
  Telephony control specification – binary (TCS BIN)
Adopted protocols
  PPP
  TCP/UDP/IP
  OBEX
  WAE/WAP

## Slide 7: Protocol Architecture
BT Radio (2.4 GHZ Freq. Band):
Modulation: Gaussian Frequency Shift Keying
Baseband: FH-SS (79 carriers), CDMA (hopping sequence from the node MAC address)
Audio: interfaces directly with the baseband. Each voice connection is over a 64Kbps SCO link. The voice coding scheme is the Continuous Variable Slope Delta (CVSD)
Link Manager Protocol (LMP): link setup and control, authentication and encryption
Host Controller Interface: provides a uniform method of access to the baseband, control registers, etc through USB, PCI, or UART
Logical Link Control and Adaptation Layer (L2CAP): higher protocols multiplexing, packet segmentation/reassembly, QoS
Service Discover Protocol (SDP): protocol of locating services provided by a Bluetooth device
Telephony Control Specification (TCS): defines the call control signaling for the establishment of speech and data calls between Bluetooth devices
RFCOMM: provides emulation of serial links (RS232). Upto 60 connections
HCI
Bluetooth Radio
Baseband
Audio
Link Manager (LMP)
L2CAP
RFCOMM
TCS
SDP
TCP/UDP
PPP
AT
Commands
OBEX
Application
OBEX: OBject EXchange (e.g., vCard)

## Slide 8: Usage Models
File transfer
Internet bridge
LAN access
Synchronization
Three-in-one phone
Headset

## Slide 9: Piconets and Scatternets
Piconet
  Basic unit of Bluetooth networking
  Master and one to seven slave devices
  Master determines channel and phase
Scatternet
  Device in one piconet may exist as master or slave in another piconet
  Allows many devices to share same area
  Makes efficient use of bandwidth

## Slide 10: Wireless Network Configurations

## Slide 11: Network Topology
Piconet = set of Bluetooth nodes synchronized to a master node
  The piconet hopping sequence is derived from the master MAC address (BD_ADDR IEEE802 48 bits compatible address)
Scatternet = set of piconet
Master-Slaves can switch roles
A node can only be master of one piconet. Why?
Piconet 1
Master
Master
Piconet 2
Scatternet
Slave

## Slide 12: Scatternets
piconets
Each piconet has one master and up to 7 slaves
Master determines hopping sequence, slaves have to synchronize
Participation in a piconet = synchronization to hopping sequence
Communication between piconets = devices jumping back and forth between the piconets

## Slide 13: Radio Specification
Classes of transmitters
  Class 1: Outputs 100 mW for maximum range
    Power control mandatory
    Provides greatest distance
  Class 2: Outputs 2.4 mW at maximum
    Power control optional
  Class 3: Nominal output is 1 mW
    Lowest power

## Slide 14: Frequency Hopping in Bluetooth
Provides resistance to interference and multipath effects
Provides a form of multiple access among co-located devices in different piconets

## Slide 15: Frequency Hopping
Total bandwidth divided into 1MHz physical channels
FH occurs by jumping from one channel to another in pseudorandom sequence
Hopping sequence shared with all devices on piconet
Piconet access:
  Bluetooth devices use time division duplex (TDD)
  Access technique is TDMA
  FH-TDD-TDMA

## Slide 16: Frequency Hopping

## Slide 17: Physical Links between Master and Slave
Synchronous connection oriented (SCO)
  Allocates fixed bandwidth between point-to-point connection of master and slave
  Master maintains link using reserved slots
  Master can support three simultaneous links
Asynchronous connectionless (ACL)
  Point-to-multipoint link between master and all slaves
  Only single ACL link can exist

## Slide 18: Bluetooth Packet Fields
Access code – used for timing synchronization, offset compensation, paging, and inquiry
Header – used to identify packet type and carry protocol control information
Payload – contains user voice or data and payload header, if present

## Slide 19: Bluetooth Piconet MAC
Each node has a Bluetooth Device Address (BD_ADDR). The master BD_ADDR determines the sequence of frequency hops
Types of connections:
  Synchronous Connection-Oriented link (SCO) (symmetrical, circuit switched, point-to-point)
  Asynchronous Connectionless Link (ACL): (packet switched, point-2-multipoint, master-polls)
Packet Format:
  Access code: synchronization, when piconet active derived from master
  Packet header (for ACL): 1/3-FEC, MAC address (1 master, 7 slaves), link type, alternating bit ARQ/SEQ, checksum
f(k)
f(k+1)
f(k+2)
f(k+3)
f(k+4)
f(k+4)
f(k+4)
f(k+7)
Master
Slave 1
Slave 2
bits
access code
packet header
payload
72
54
0-2745
bits
MAC address
type
flow
ARQN
SEQN
HEC
3
4
1
1
1
8
Notes: Slot duration: 625seconds
Why don’t we transmit during all the slot?

## Slide 20: Types of Access Codes
Channel access code (CAC) – identifies a piconet
Device access code (DAC) – used for paging and subsequent responses
Inquiry access code (IAC) – used for inquiry purposes

## Slide 21: Access Code
Preamble – used for DC compensation
  0101 if LSB of sync word is 0
  1010 if LSB of synch word is 1
Sync word – 64-bits, derived from:
  7-bit Barker sequence
  Lower address part (LAP)
  Pseudonoise (PN) sequence
Trailer
  0101 if MSB of sync word is 1
  1010 if MSB of sync word is 0

## Slide 22: Packet Header Fields
AM_ADDR – contains “active mode” address of one of the slaves
Type – identifies type of packet
Flow – 1-bit flow control
ARQN – 1-bit acknowledgment
SEQN – 1-bit sequential numbering schemes
Header error control (HEC) – 8-bit error detection code

## Slide 23: Payload Format
Payload header
  L_CH field – identifies logical channel (i.e., LMP msg, L2CAP msgs)
  Flow field – used to control flow at L2CAP level
  Length field – number of bytes of data
Payload body – contains user data
CRC – 16-bit CRC code

## Slide 24: Error Correction Schemes
1/3 rate FEC (forward error correction)
  Used on 18-bit packet header, voice field in HV1 packet
2/3 rate FEC
  Used in DM packets, data fields of DV packet, FHS packet and HV2 packet
ARQ
  Used with DM and DH packets

## Slide 25: ARQ Scheme Elements
Error detection – destination detects errors, discards packets
Positive acknowledgment – destination returns positive acknowledgment
Retransmission after timeout – source retransmits if packet unacknowledged
Negative acknowledgment and retransmission – destination returns negative acknowledgement for packets with errors, source retransmits

## Slide 26: Types of packets
SCO packets: Do not have a CRC (except for the data part of DV) and are never retransmitted. Intended for High-quality Voice (HV).
ACL packets: Data Medium-rate (DM) and Data High-rate (DH)
Type
Payload
(bytes)
FEC
CRC
Symm.
max-rate kbps
HV1
10
1/3
No
64
HV2
20
2/3
No
64
HV3
30
No
No
64
DV
10+(1-10)D
2/3D
Yes D
64+57.6D
Type
Payload
(bytes)
FEC
CRC
Symm.
max-rate kbps
Asymm.
max-rate (DL/UL)
DM1
0-17
2/3
Yes
108.8
108.8/108.9
DM3
0-121
2/3
Yes
258.1
387.2/54.4
DM5
0-224
2/3
Yes
286.7
477.8/36.3
DH1
0-27
No
Yes
172.8
172.8/172.8
DH3
0-183
No
Yes
390.4
585.6/86.4
DH5
0-339
No
Yes
433.9
723.2/185.6

## Slide 27: Logical Channels
Link control (LC)
Link manager (LM)
User asynchronous (UA)
User isochronous (UI)
Use synchronous (US)

## Slide 28: Channel Control
States of operation of a piconet during link establishment and maintenance
Major states
  Standby – default state
  Connection – device connected

## Slide 29: Channel Control
Interim substates for adding new slaves
  Page – device issued a page (used by master)
  Page scan – device is listening for a page
  Master response – master receives a page response from slave
  Slave response – slave responds to a page from master
  Inquiry – device has issued an inquiry for identity of devices within range
  Inquiry scan – device is listening for an inquiry
  Inquiry response – device receives an inquiry response

## Slide 30: State Transition Diagram

## Slide 31: Inquiry Procedure
Potential master identifies devices in range that wish to participate
  Transmits ID packet with inquiry access code (IAC)
  Occurs in Inquiry state
Device receives inquiry
  Enter Inquiry Response state
  Returns FHS (Frequency Hop Synchrnonization) packet with address and timing information
  Moves to page scan state

## Slide 32: Page Procedure
Master uses devices address to calculate a page frequency-hopping sequence
Master pages with ID packet and device access code (DAC) of specific slave
Slave responds with DAC ID packet
Master responds with its FHS packet
Slave confirms receipt with DAC ID
Slaves moves to Connection state

## Slide 33: Slave Connection State Modes
Active – participates in piconet
  Listens, transmits and receives packets
Sniff – only listens on specified slots
Hold – does not support ACL packets
  Reduced power status
  May still participate in SCO exchanges
Park – does not participate on piconet
  Still retained as part of piconet

## Slide 34: States of a Bluetooth Device (PHY layer)
STANDBY
inquiry
page
connected
transmit
PARK
HOLD
SNIFF
unconnected
connecting
active
low power
BT device addressing:
BD_ADDR (48 bits)
AM_ADDR ( 3bits): ACTIVE, HOLD, or SNIFF
PM_ADDR (8 bits): PARK Mode address (exchanged with the AM_ADDR when entering PARK mode)
AR_ADDR (8 bits): not unique used to come back from PARK to ACTIVE state
ACTIVE (connected/transmit): the device is uniquely identified by a 3bits AM_ADDR and
is fully participating
SNIFF state: participates in the piconet only within the SNIFF interval
HOLD state: keeps only the SCO links
PARK state (low-power): releases AM_ADDR but stays synchronized with master

## Slide 35: Bluetooth Device Operation [Page 105 of 1084]
Inquiry:
  Goal: aims at discovering other neighboring devices
  Inquiring node:
    Sends an inquiry message (packet with only the access code: General Inquiry Access Code: GIAC or Dedicated IAC: DIAC). This message is sent over a subset of all possible frequencies.
    The inquiry frequencies are divided into two hopping sets of 16 frequencies each.
    In inquiry state the node will send upto NINQUIRY sequences on one set of 16 frequencies before switching to the other set of 16 frequencies. Upto 3 switches can be executed. Thus the inquiry may last upto 10.24 seconds.
  To be discovered node:
    Enters an inquiry_scan mode: listens over one frequency for Tw_inquiry_scal time
    When hearing the inquiry_message (and after a backoff procedure) enter an inquiry_response mode: send a Frequency Hop Sync (FHS) packet (BD_ADDR, native clock)
  After discovering the neighbors and collecting information on their address and clock, the inquiring node can start a page routine to setup a piconet

## Slide 36: Bluetooth Device Operation (Cont’d) [Page 102 of 1084]
Page:
  Goal: e.g., setup a piconet after an inquiry
  Paging node (master):
    Sends a page message (i.e., packet with only Device Access Code of paged node) over 32 frequency hops (from DAC and split into 2*16 freq.)
    Repeated until a response is received
    When a response is received send a FHS message to allow the paged node to synchronize
  Paged node (slave):
    Listens on its hopping sequence
    When receiving a page message, send a page_response and wait for the FHS of the pager

## Slide 37: Bluetooth Audio
Voice encoding schemes:
  Pulse code modulation (PCM)
  Continuously variable slope delta (CVSD) modulation
Choice of scheme made by link manager
  Negotiates most appropriate scheme for application

## Slide 38: Bluetooth Link Security
Elements:
  Authentication – verify claimed identity
  Encryption – privacy
  Key management and usage
Security algorithm parameters:
  Unit address
  Secret authentication key (128 bits key)
  Secret privacy key (4-128 bits secret key)
  Random number

## Slide 39: LMP PDUs
General response
Security Service
  Authentication
  Pairing
  Change link key
  Change current link key
  Encryption

## Slide 40: LMP PDUs
Time/synchronization
  Clock offset request
  Slot offset information
  Timing accuracy information request
Station capability
  LMP version
  Supported features

## Slide 41: LMP PDUs
Mode control
  Switch master/slave role
  Name request
  Detach
  Hold mode
  Sniff mode
  Park mode
  Power control

## Slide 42: LMP PDUs
Mode control (cont.)
  Channel quality-driven change between DM and DH
  Quality of service
  Control of multislot packets
  Paging scheme (1 mandatory + optional)
  Link supervision (max time before declaring the failure of a link)

## Slide 43: L2CAP
Provides a link-layer protocol between entities with a number of services
Relies on lower layer for flow and error control
Makes use of ACL links, does not support SCO links
Provides two alternative services to upper-layer protocols
  Connectionless service
  Connection-mode service

## Slide 44: L2CAP Logical Channels
Connectionless
  Supports connectionless service
  Each channel is unidirectional
  Used from master to multiple slaves
Connection-oriented
  Supports connection-oriented service
  Each channel is bidirectional
Signaling
  Provides for exchange of signaling messages between L2CAP entities

## Slide 45: L2CAP Packet Fields for Connectionless Service
Length – length of information payload, PSM fields
Channel ID – 2, indicating connectionless channel
Protocol/service multiplexer (PSM) – identifies higher-layer recipient for payload
  Not included in connection-oriented packets
Information payload – higher-layer user data

## Slide 46: Signaling Packet Payload
Consists of one or more L2CAP commands, each with four fields
  Code – identifies type of command
  Identifier – used to match request with reply
  Length – length of data field for this command
  Data – additional data for command, if necessary

## Slide 47: L2CAP Signaling Command Codes

## Slide 48: L2CAP Signaling Commands
Command reject command
  Sent to reject any command
Connection commands
  Used to establish new connections
Configure commands
  Used to establish a logical link transmission contract between two L2CAP entities

## Slide 49: L2CAP Signaling Commands
Disconnection commands
  Used to terminate logical channel
Echo commands
  Used to solicit response from remote L2CAP entity
Information commands
  Used to solicit implementation-specific information from remote L2CAP entity

## Slide 50: Flow Specification Parameters
Service type
Token rate (bytes/second)
Token bucket size (bytes)
Peak bandwidth (bytes/second)
Latency (microseconds)
Delay variation (microseconds)