## Slide 1: Wireless Multihop Ad Hoc Networks
Guevara Noubir
noubir@ccs.neu.edu

## Slide 2: Infrastructure vs. Ad Hoc Wireless Networks
Infrastructure networks:
  One or several Access-Points (AP) connected to the wired network
  Mobile nodes communicate through the AP
Ad hoc network:
  Mobile nodes communicate directly with each other
  Multi-hop ad hoc networks: all nodes can also act as routers
Hybrid (nodes relay packets from AP):
  Goal: increase capacity, reduce power consumption, and guarantee a minimum service
Notes: Infrastructure networks:
Hybrid: Reduce infrastructure cost…
Pure Ad Hoc has limited application, pure infrastructure can be expensive (specially over high frequency bands),
Hybrid is reasonable: RF transceiver can cover areas from few meters to 20 miles (at different data rates…)

## Slide 3
Notes: Multi-interface nodes may allow to have two cluster of nodes operating over different frequencies (reducing collisions) an multi-interface node operating as a gateway.

## Slide 4: Constraints
Limited radio spectrum
Broadcast Medium (collisions)
Limited power available at the nodes
Limited storage memory
Connection QoS requirements (e.g., delay, packet loss)
Unreliable network connectivity (depends on the channel)
Dynamic topology (i.e., mobility of nodes, density)
Need to provide a full coverage
Need to enforce fairness
Notes: Problems at all layers.

## Slide 5: Parameters
Use of various coding/modulation schemes
Use of packets fragmentation
Use of various transmission power level
Use of smart antennas and MIMO systems
Use of multiple RF interfaces (multiple IF characteristics)
Clustering and backbone formation
Planning of the fixed nodes location
Packets scheduling schemes
Application adaptivity

## Slide 6: Adaptivity and Cooperation
Classical networking stacks have only minimum interaction between adjacent layers
Multi-hop wireless ad hoc networks require more cooperation between layer because:
  Channel variation and network topology changes affect the application
  Routing versus single hop communication considerably affects the medium access control (MAC) performance
  Collisions versus channel fading affects both the physical layer and the MAC
  Battery power has implications on all layers
Notes: Network layer needs info on status of the channel to nodes to decide on one or multiple hop transmission

## Slide 7: Adaptive Coding
Example:
  ½ rate convolutional code (K=5) versus uncoded communication
  Channel with two states: Eb/N0 = 6.8 dB or 11.3 dB (AWGN), L=200 Bytes
Need to estimate the channel and adapt to it
Differentiate between congestions and a bad channel condition
Use of Hybrid-ARQ?
Eb/N0
BER
FER
Nb_Transmit
Total_Tx_Bytes
UC
½ CC
UC
½ CC
UC
½ CC
UC
½ CC
6.8dB
10-3
10-7
0.8
1.6 10-4
5
~ 1
5*200
2*200
11.3dB
10-7
~ 0
1.6 10-4
~ 0
~ 1
~ 1
200
2*200
Notes: Coding is good but only if you use it when necessary. Otherwise you have useless redundancy

## Slide 8: Adaptive Fragmentation
Example:
  To transmit a frame of length 200 Bytes, we can fragment into 4 frames of length 50 Bytes (+ 10 Bytes overhead)
Need to estimate the channel and adapt to it
BER
FER
Nb_Transmit
Total_Tx_Bytes
(incl. overhead)
L=60B
L=200B
L=60B
L=200B
L=60B
L=200B
10-3
0.38
0.8
1.6
5
384
1000
10-7
~ 0
~ 0
~ 1
~ 1
240
200
Notes: Later on we will see how we can adapt by implicitly estimating the channel

## Slide 9: Multiple Power Levels
Using multi-hop transmission (h hops) and reducing the transmission power accordingly
  Increases capacity (factor of h)
  Reduces overall power consumption
  (by a factor of h)
In asymmetric environments
  Low power node can encode data
  and transmit it at low power
  Powerful nodes can decode use
  higher transmission power

## Slide 10: Problems of Multi-Hop Routing
Routing:
  How to maintain up-to-date information on the network topology? Routing messages overhead
  How to determine number of hops
  How to estimate buffers size
Higher delay
Risk of congestion on nodes

## Slide 11: Practical Approaches
Solving sub-problems independently
  Improving TCP to be wireless aware
  Routing in multi-hop wireless ad hoc networks: DSDV, DSR, AODV, TORA, FSR
    Not power or resource aware. Single hop whenever possible (no interaction with the MAC of higher layers)
  Fragmenting packets according to the channel performance
  Adapting coding/modulation scheme to the channel
  Adapting transmission power to destination
There is a need for a global approach:
  Combine: transmission power, coding, and fragmentation
  Add routing
  Add medium access control
Engineering perspective: what minimal subset of functionalities do we need to implement to achieve near optimal performance?
  What minimal set of coding/modulation schemes? What power levels do we need?
Notes: Some of these are not even implemented in real systems
It is not easy to implement multi-level power levels:
802.11 proposes 8 levels: only one is implemented (to our knowledge)
Bluetooth: proposes 3 levels only one is implemented
Trying to modify everything is utopic defacto-standards/architectures (TCP/IP) are very difficult to change

## Slide 12: Routing Protocols: DSDV
Destination-Sequenced Distance Vector:
  Each node maintains a routing table listing:
    <next-hop, metric, SeqNum>:
    The favored route is changed if a new route with higher SeqNum is received, or if the new route has equal SeqNum and lower metric
  Nodes send advertisement with evenly increased SeqNum
  When a node detects a broken link he sends an advertisement with  metric and SeqNum=PrevSeqNum+1
  Damping fluctuations:
    Fluctuations are due to out-of-order arrival of route advertisement
    Proposed solution: maintain a settling time estimation for routes
    Route with an  metric are advertised without delay

## Slide 13: Dynamic Source Routing I <draft-ietf-manet-dsr-05.txt:2001>
Split routing into discovering a path and maintaining a path
Discover a path
  only if a path for sending packets to a certain destination is needed and no path is currently available
Maintaining a path
  only while the path is in use, one has to make sure that it can be used continuously
No periodic updates needed!

## Slide 14: Dynamic Source Routing II
Path discovery
  broadcast a Route Request packet with destination address and unique ID
  if a station receives a broadcast packet
    if the station is the receiver (i.e., has the correct destination address) then return the packet to the sender (path was collected in the packet): Route Reply
    if the packet has already been received earlier (identified via ID) then discard the packet
    otherwise, append own address and broadcast packet
  sender receives packet with the current path (address list)
Optimizations
  limit broadcasting if maximum diameter of the network is known
  caching of address lists (i.e. paths) from passing packets (overhearing)
    stations can use the cached information for path discovery (own paths or paths for other hosts)

## Slide 15: Dynamic Source Routing III
Maintaining paths
  after sending a packet
    wait for a layer 2 acknowledgement (if applicable)
    listen into the medium to detect if other stations forward the packet (if possible)
    request an explicit acknowledgement
  if a station encounters problems it can inform the sender of a packet or look-up a new path locally

## Slide 16: Routing Protocols: DSR and FSR
Dynamic Source Routing has two mechanisms:
  Route Discovery:
    A Route Request packet is flooded through the network
    Route reply is sent back to the source
    Optimization: cache of source routes (learned or overheard)
  Route Maintenance:
    On discovery of a broken link (e.g., nodes moved out of range), a Route Error is sent to the source => use an alternate cached route or rerun Route Discovery
Fisheye State Routing:
  Maintains link state information with a frequency that depends on the fisheye scope distance
  Nodes do not need to have a very precise information on far away nodes

## Slide 17: Parameters of IEEE802.11
IEEE802.11 has three mechanisms that can be used to improve performance under dynamic channels:
  Fragmentation (also used to avoid collision)
  Multiple coding/modulation schemes (8 schemes)
  8 power levels
Multiple coding/modulation schemes will be available with 802.11a products over 5GHz
Currently parameters are statically configured

## Slide 18: Interference-Based Routing
Routing based on assumptions about interference between signals
S1
N5
N3
N4
N1
N2
R1
R2
N6
N8
S2
N9
N7
neighbors
(i.e. within radio range)

## Slide 19: Examples for interference based routing
Least Interference Routing (LIR)
  calculate the cost of a path based on the number of stations that can receive a transmission
Max-Min Residual Capacity Routing (MMRCR)
  calculate the cost of a path based on a probability function of successful transmissions and interference
Least Resistance Routing (LRR)
  calculate the cost of a path based on interference, jamming and other transmissions
LIR is very simple to implement, only information from direct neighbors is necessary

## Slide 20: Clustering
Goal:
  Reduce channel contention
  Form routing backbone to reduce network diameter
  Abstract network state to reduce its quantity and its variability
Various approaches to clustering
  Started in the 70s with Packet Radio Network (PRNet) sponsored by DARPA
Notes: Goal: respond rapidly to network variations (topology, link quality, …) and minimize resource consumption. This is the general framework for all wireless networks. How does clustering answer this need?
Clusters try to impose a control structure on the network of mobile nodes.

## Slide 21: Theoretical Results
Capacity of a wireless network [Gupta & Kumar 2000]
  n identical randomly located nodes each capable of transmitting W bits can only achieve a throughput of
  n optimally placed nodes with an optimal traffic pattern and an optimal transmission power can only achieve
Notes: Theta come from the Pmax/Pmin or SNR
If you remember the gain we had using h hops. In a two dimensional space if we want to have h hops => N = h^2…

## Slide 22: Clustering for Transmission Management
Goal: reduce contention
Cluster = clusterhead + gateways + ordinary nodes
Roles:
  Clusterhead: schedules traffic, allocates resources (tokens, emits busy tone, etc.). Similar to the master in a Bluetooth piconet.
  Gateways: interconnect clusters
  Ordinary nodes are 1-hop away from a clusterhead and 2-hops away from other members in the cluster
Tasks:
  Connectivity discovery
  Election of clusterheads
  Agree on Gateways
Notes: Refs: [Baker 1981, Ephremides 1987, Gerla 1995, Lin 1997, Raj?…

## Slide 23: Clustering for Transmission Management (Cont)
Clusterhead election:
  Centralized/distributed algorithms
  Node identifier/degree based
  Principles:
    Centralized: (1) elect the highest ID node and create a corresponding cluster, repeat step (1) with nodes not already members of a cluster
    Distributed:
      a node elects itself as cluster head if it has the highest ID among its neighbors
      otherwise elect a neighbor that is not member of another cluster
  Leads to disjoint clusters
Gateways:
  If connected to > 1 cluster => gateway candidate
  If num_hops (CH1) = 1 & num_hops(CH2) = 2 =>GW1 --- GW2
  When multiple candidates to connect two clusters, choose GW with highest ID
Notes: Algorithms do not use connectivity flexibility

## Slide 24: Clustering for Transmission Management (Cont)
Mobility:
  Most algorithms do not adjust to mobility. They recompute the cluster.
  Recent algorithms:
    change clusterhead status when two clusterheads become neighbors
    [Gerla-Lin 1995, 1997]: cluster maintenance
Routing:
  To avoid clusterhead congestion and improve robustness, routing is done over the flat network

## Slide 25: Clustering for Backbone Formation
Wireless multiphop networks have high end-to-end delay:
  link-layer ARQ, MAC delay, FEC/spreading, tx/rx switching time
Clustering can reduce the end-to-end delay by allowing faster forwarding through the clusterheads backbone
Approaches:
  Near-Term Digital Radio Network (NTDR) [Zavgren 1997]
  Virtual Subnet Architecture [Sharony 1996]

## Slide 26: Near-Term Digital Radio Network (NTDR)
Goal: support mobile tactical communication
Architecture: clusterheads = gateways+single-hop nodes
Communication:
  All 2-hop packets go through the clusterheads backbone
  Two frequencies: intra-cluster band + inter-cluster band
Clusterhead election:
  Clusterheads send a beacon (organization, members, TxPwrL, PL to nodes)
  Nodes elect themselves if: (1) do not receive a beacon, (2) receives beacons with different partition numbers
Preventing multiple clusterhead creation:
  Wait a random amount of time before self-election as clusterhead
  After self-election, immediately issue beacons
  Eliminate superfluous clusterheads without partitioning the network

## Slide 27: NTDR (Cont)
Cluster affiliation criteria:
  Node and clusterhead are in the same organization
  Low path loss (conserves energy)
  Resulting cluster has a small size
Canceling affiliation:
  Clusterhead relinquishes its role
  Broken link (or low quality link)
On membership change all clusterheads are updated
Routing:
  Use a link state protocol: Dijkstra’s Shortest Path First algorithm
  Resistance metric: minimize interference experienced by packets
  Does not scale for high mobility networks because of flooding cost

## Slide 28: Virtual Subnet Architecture
Goal: fault-tolerant connectivity and load balancing
Architecture:
  Disjoint clusters: physical subnets (at most P)
  Physical subnets are clustered into virtual subnets (at most Q)
  Virtual subnets ideally span all physical subnets
  Virtual subnets and neighboring subnets operate over different frequencies
  Nodes addresses: location dependent addresses (physical subnet, virtual subnet) + location independent address
After affiliation to a physical/virtual subnet, the node advertises its new address to the physical/virtual subnet
To determine the location dependent address of a node:
  Distribute an address query to the physical subnet. Use the virtual subnets membership information of the physical subnet
  If unsuccessful distribute the address query to the virtual subnet

## Slide 29: Virtual Subnet Architecture
Routing strategies:
  Direct routing:
    Forward the packet to a node x that is both in the source physical subnet and destination virtual subnet
    Forward the packet through the virtual subnet to reach the physical subnet of the destination
  Long-path routing (under high mobility): randomly distribute the routes over the space of possible routes
    Forward the packet through a virtual subnet represented by a node in the source physical subnet, or
    Forward the packet through the physical subnet of a node in the virtual subnet of the source
    P+Q-1 possible paths

## Slide 30: Clustering for Routing Efficiency
Quasi-hierarchical routing
  Each node learns the next node to use to reach all level-i clusters within its (i+1) ancestral level
  Reduces the amount of routing information from O(N) to O(mCmax)
  Both distance-vector and link-state approaches
  Minimized forwarding tables and optimal routes:
    Number of level-i clusters in each level-(i+1) = e, and ln N levels
    Quasi-hierarchical routing routes -> optimum (under ideal assumptions)
Strict hierarchical routing
  Each node learns the next level-i cluster to use in order to reach each level-i cluster within its level-i+1 cluster
  Each node learns which level-i clusters lie on the boundary of its level-(i+1) cluster
  Read page 109 (A Prototypical Scheme)

## Slide 31: Building a Clustering Hierarchy
Objectives:
  Minimizing the amount of routing information
  Maximize connectivity within each cluster
  Localize high-intensity traffic within one cluster
  Minimizing the number of intercluster links
  Maximizing the stability of intercluster links
  Minimizing the difference between the hierarchical route and the optimal route
Possible constraints:
  Upper/lower limit of the number of childs
  Upper limit on the diameter of each cluster
  Constant number of childs

## Slide 32: Limitations of Current Clustering Algorithms
Most clustering algorithms do not consider the flexibility/constraints of radio frequency communication:
  Connectivity is not rigid but can be controlled through power-control
  Leader consume more energy then ordinary nodes
Relation between MAC, power-control and coding:
  Coding generates more time interference (collisions?), high power generates more space interference (SNIR)
Hybrid networks require to consider fairness more seriously:
  Nodes in the vicinity of the AP would experience more traffic than nodes on the periphery